## Slide 1: Meshing Schemes
Steven Owen
CUBIT™ 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
7
SAND2022-15021 PE

## Slide 2
The CUBIT™ Workflow
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 3
CUBIT™ Provides a number of different surface mesh schemes. Choosing the best scheme depends on the shape and number of curves in the surface. Your choice also depends on how you plan to mesh the volume.
Surface Meshing Schemes
TriMesh
Map
SubMap
Pave
TriPrimitive
Polyhedron
Hole
Circle

## Slide 4
CUBIT™ Provides a number of different volume mesh schemes. Similar to Surface Scheme Selection, Volume Scheme Selection is based on the shape of the geometry and the requirements of the analysis code.
Map
Sweep
SubMap
Polyhedron
Sphere
TetMesh
Sculpt Parallel
Volume Meshing Schemes
TetPrimitive

## Slide 5
Volume and Surface Schemes can be manually applied from the Property Page or from the CUBIT™ Volume/Surface Meshing Command Panels.
By choosing Automatically Calculate, CUBIT™ will attempt to select the best mesh scheme for the surface
Scheme priority will be set based on characteristics of geometry.
CUBIT™ Property Page
Auto Scheme Selection
1. Map
2. SubMap
3. Sweep
1. Map
2. SubMap
4. Pave
3. TriPrim
CUBIT™ Surface Meshing
Command Panel
Volumes
Surfaces

## Slide 6: Exercise 7.1 Meshing Schemes
Reset and import schemes.sat
Set mesh size to 1.00
Use the Auto Calc and mesh all surfaces and volumes and check the auto-selected schemes
Reset volumes and experiment with different surface and volume meshing schemes. For example:
1
2
3
4
mesh volume all
surface 9 scheme circle
mesh surface 9
mesh vol 2
surface 17 scheme hole rad_intervals 4
mesh surface 17
mesh vol 3
Volume 2
Volume 3
volume 5 scheme polyhedron
mesh vol 5
Volume 5

## Slide 7
Source surfaces
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source Surfaces
One or more surfaces
Can be meshed with any Quad Scheme (Pave, Map)
Target Surface
Must be a single surface
Must be unmeshed
Matches topology of source surfaces
Sweep Scheme

## Slide 8
Linking surfaces
Linking surfaces
Linking surfaces
Linking surfaces
Linking Surfaces
Must be “Mappable”
Connect Sources with Target
Sweep Scheme

## Slide 9
Most frequently used meshing scheme
Normally requires geometry to be decomposed to apply sweeping (webcutting)
Sweep Scheme

## Slide 10
Setting Source and target Surfaces
1
2
3
4
Navigate to Scheme Selection Command Panel
Shortcut from property panel to scheme selection
Choose Sweep Scheme
Pick Sources and Targets
Apply Scheme
1
2
3
4
1
Sweep Scheme

## Slide 11: Exercise 7.2 Sweeping
Import “schemes.sat”
2
3
1
4
Isolate volume 14
Sweep Option 1:
Use the sweep scheme command panel to set source and target surfaces so that resulting mesh looks like Sweep Option 1
Sweep Option 2:
Do the same for Sweep option 2.
(Important: Use 3 source surfaces and one target surface)
Volume 14
Sweep Option 1
Sweep Option 2

## Slide 12
Ideal for non-mechanical/
organic shapes
Overlay Grid Method
Uses Cartesian Grid as Base Mesh
Adjusts nodes to geometry
Inserts Layer of Hexes
But can be used for any geometry
Sculpt

## Slide 13
Sculpt is a separate companion application to CUBIT™ .
Can be run from CUBIT™ GUI or in batch from OS command line
Parallel application uses MPI to run on multiple cores/processors
See Cubit 200 for more details/exercises
Does not use Scheme, instead uses Sculpt Parallel command.
Sculpt
3
1
2
If you get an error
Check your working directory with “pwd”
Ensure your working directory has write permissions
Change directories or create a new directory

## Slide 14: Exercise 7.3 Sculpt
Import the stl file “eros_asteroid.stl” (change the file filter to “stl”)
Preview the overlay grid resolution
Mesh
Use the slice tool to view the interior hexes
Delete mesh and experiment with alternate sizes
2
1
Navigate to sculpt panel
3
4
3
1
5
5
4
3
6

## Slide 15
Arbitrary geometry
Mostly push-button/automatic
May still require geometry clean-up
Tetmesh Scheme

## Slide 16: Exercise 7.4 Tet Meshing
Import model
Import ACIS file driver.sat OR cad6.sat
driver.sat
cad6.sat
1
1

## Slide 17: Exercise 7.4 (continued) Tet Meshing
Mode - Mesh
Entity - Volume
Action - Mesh
Select Volume to Mesh (1)
Choose Tetmesh Scheme
Apply the Tetmesh Scheme
Click the Mesh Button
OR
Volume 1 scheme tetmesh
Mesh Volume 1
From Cubit Command Window
1
2
3
4
5
6
7
1
2
3
4
5
6
7