## Slide 1: Defeaturing
Steven Owen
CUBIT™ 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
8
SAND2022-15021 PE

## Slide 2
The CUBIT™ Workflow
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 3
Defeaturing
Geometry from CAD design tools can include many unnecessary features
May be too complex for hex meshing
May require too many elements resulting in long run times
Customer may only want approximate, fast turn-around
32,559 tets
397,258 tets
CAD part from designer
Defeaturing
CAD part for simulation
595 surfaces
1506 curves
994 vertices
3

## Slide 4
GUI Tools
Select Surface in graphics window
Right Click
A list of available selection tools will be offered based on the selected surface
Select Similar | Selects other entities with the same geometric description (volume, area, length, topology)
Select Blend Chain | Selects other surfaces in the same blend chain that have the same radius of curvature
Select Cavity | Selects other surfaces in the same cavity collection. Surfaces bounded by curves where the external angle is greater than 180 degrees.
Select Hole | Selects other surfaces that are within the same hole definition
Select by Name | Selects other entities with the same name. Includes entities with the same name prefix prior to the "@" character if it exists.

## Slide 5: Exercise 8.1 Defeaturing with the GUI
Import the acis file “anc101.sat”
Use the GUI selections and remove operation to simplify so it looks like the image below
Measure the volume before defeaturing
Use the sweep scheme to mesh the defeatured volume
1
2
3
4
list volume 1 geometry
Make a note of the volume of volume 1
Find the volume of the defeatured geometry. Compute the percent difference in volume
5

## Slide 6
Geometry Power Tools are located in the second tab of the PowerTools window.
Geometry Power Tool

## Slide 7
Pick volumes to analyze
Run geometry analysis (disabled until Options… selected)
Geometry analysis output
Additional Geometry Operations
Update analysis after each geometry operation
Select Geometry Diagnostics (Click Here first)
Show Documentation
Display Solution Window
Geometry Power Tool Panel

## Slide 8
Add Additional Diagnostics that use machine learning
Threshold values for Diagnostics
Diagnostic Checks (select only those you want to perform)
Generate diagnostic threshold values automatically
Select Done to return to Power Tool
Fast way to select or unselect diagnostics
Geometry Power Tool Options Panel

## Slide 9
Import anc101.sat
Enter “all” or “1” for volumes to analyze
Select “Options…”
Select “Auto Size”
Select “Select All”
Select “Done”
Select “Analyze”
You should see results in the power tool that look similar to those shown.
Geometry Power Tool Example
1
2
3
4
5
6
7
2
3
7
4
5
6

## Slide 10
Click triangle to expand “Small Surfaces” Diagnostic
Select Surface 94
Right Click to display context menu
Select “Fly In” to zoom into surface 94
Surface 94
Visualize/Selection Options
Relevant Cubit Commands (Jump to Command Panel)
Remove small curves and surfaces
Geometry Power Tool Example
1
2
3
4

## Slide 11
Surface 94
Select Remove Surface
(Command Panel Appears)
Click Apply
Before Surface Remove
After Surface Remove
Note: Surface 94 is auto populated in pickwidget
Remove small curves and surfaces
1
2
Geometry Power Tool Example

## Slide 12
Click Power Tools Tab to return to Geometry Power Tool
Note: Surface 94 and it’s small curves are shown (deleted)
Click Analyze to regenerate diagnostics
Note: Check Auto Update to auto. regenerate every time model changes (slow for large models)
Try the same procedure to remove surface 95
Remove small curves and surfaces
1
2
1
2
3
Geometry Power Tool Example

## Slide 13
Custom Solutions – Remove bad angles
Select Show Solutions
Custom Solution Window
Shows specific solutions for selected entity (vertex 95)
Expand “Bad Vertex Angles” Diagnostic
Select vertex 95 and “Fly-in”
Single Click: Preview and visualize custom solutions
Blunt Tangency Add Material Angle 15
Blunt Tangency Remove Material Angle 30
Collapse Angle 45
Double Click: Execute the solution
Note: Right Click on Solution for additional options (Jump to command panel)
Try same procedure on Vertex 94
Geometry Power Tool Example
1
2
3
4
5
6

## Slide 14
Geometry Traits – Remove chamfer
Expand “Chamfer Chains” Diagnostic
Select and fly into Chain 1
Double Click “Remove Surface” Solution
Geometry Power Tool Example
1
2
3

## Slide 15
Geometry Traits – Remove holes
Note: Holes are not currently displayed because they all have a radius larger than the “hole radius threshold”. Go back to the Options panel to manually change this value.
Click on the Options button
Enter “10” for the “Hole Radius” threshold
Click Done
Click Analyze
Right Click on Holes and “Select All”
Use the “Remove All Holes…” menu option to delete holes with one command
Geometry Power Tool Example
1
2
3
4
5
6

## Slide 16: Exercise 8.2 Geometry Power Tool
Import acis “knuckle.sat”
Mesh with tets using size 2.0
Delete Mesh
Use the Geometry Power Tool to assist in defeaturing. Suggested operations:
Remove Close Loops
  Surface 17
  Surface 15
Heal Bad Geometry
  Bad Curves
Mesh with tets using size 2.0
Delete Mesh and save acis geometry file “knuckle-defeatured.sat”
2
1
3
4
5
6
Original Geometry
Defeatured Geometry

## Slide 17
Predict local mesh quality
  Scaled Jacobian
  In-Radius
  Deviation
Find the most problematic features in the CAD Model
1
For a given local geometry operation
  Remove Surface
  Tweak Replace Surface
  Composite Surfaces
  Collapse Curve
  Etc..
Predict local mesh quality after operation
  Scaled Jacobian
  In-Radius
  Deviation
Find solution that yields best mesh quality
2
For a given local topology
  Small Curve
  Small Surface
  Sharp Angle at Vertex
17
Defeaturing using Machine Learning
tweak remove topology curve
tweak remove topology surface
blunt tangency
remove surface
tweak replace surface
composite surfaces
collapse curve
begin state
end state
17

## Slide 18
Click to add additional diagnostics that use machine learning
Settings used only with Machine Learning Diagnostics
Diagnostics available without ML Models Loaded
1. Predict tet mesh quality on the CAD before meshing
2. Classify volumes based on their predicted function
Two new diagnostics that use Machine Learning:
Without ML
With ML
Geometry Power Tool with Machine Learning

## Slide 19
Import anc101.sat
Enter "all" or "1" for volumes to analyze
Select "Options…"
Select "Auto Size"
Select "Tetmesh Poor Quality Metrics"
Unselect the remainder of the diagnostics
Select "Done"
Select "Analyze"
Geometry Power Tool ML Example
1
2
3
5
6
7
2
3
4
4
5
6
7
8
8

## Slide 20
List of entities predicted to have poor Scaled Jacobian
List of entities predicted to have poor Inradius ratio
r
Predicted minimum Scaled Jacobian near Curve 64
Predicted minimum Inradius ratio near Curve 64
Curve 64
Geometry Power Tool ML Example

## Slide 21
Click Show Solutions
List of proposed solutions for Curve 64 ordered by Scaled Jacobian prediction
Best predicted Solution: Remove Surface 94
Predicted Scaled Jacobian: 0.3977
ML generated Solutions for Curve 64
Right Click:
Execute the solution
Jump to Command Panel
Visualize solution
Single Click: Preview Solution
Double Click: Execute Solution
1
2
Geometry Power Tool ML Example
2

## Slide 22: Exercise 8.3 ML Defeaturing
Import the acis file B3.sat
Mesh with tets using a size of 1.0
Display and record minimum scaled Jacobian and/or Inradius metric. Note the minimums and where the worst quality elements occur
Delete the mesh
Use the Geometry Power Tool with ML to defeature the model
Mesh the volume again and check mesh quality. How has the mesh quality changed
1
2
3
4
5
6