## Slide 1: Mesh Sizing
Steven Owen
CUBIT™ 200 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
9
SAND2022-15142 PE

## Slide 2
The Basic CUBIT™ Process
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 3
Auto Mesh Sizing
Move slider to see preview of mesh on curves
No need to know exact size of elements
Uses heuristic to compute size of element
If no size has been set, CUBIT™ will compute an auto mesh size=5
Auto size = 7
Auto size = 5
Auto size = 1

## Slide 4
Curve Mesh Sizing
curve 6
import acis "plate-with-hole.sat"
curve 6 interval 5
mesh vol 1
curve 6
delete mesh
curve 1 size 0.1
curve 3 7 12 14 size 2
curve 6 int 5
mesh vol 1
curve 3
curve 14
curve 12
curve 7
curve 1
Mesh size and interval is an “attribute” of the curve
Remains persistent unless reset
reset curve

## Slide 5
Vertex Mesh Sizing
reset vol 1
vertex 8 size 0.1
vol 1 size 2
vol 1 scheme tetmesh
mesh vol 1
vertex 8
curve 1
delete mesh
vertex 7 size 0.1
curve 1 size 0.1
mesh vol 1
Vertex sizing can be used with tri and tet meshing (not quad or hex meshing)
vertex 8
vertex 7
curve 7
delete mesh
curve 7 size 2
mesh vol 1

## Slide 6
Exercise 9.1 Geometry Entity Mesh Sizing
Import acis “crank.sat”
Set scheme to tetmesh
Mesh using auto sizing to mesh at finest resolution (factor 1)
Set internal hole surfaces (5 6 7 8 9) to 1 and the volume to size 3 and mesh
Mesh using auto sizing to coarsest resolution (factor 10)
1
2
3
4
5
surface 5,6,7,8
surface 9

## Slide 7
Tetmesh Controls on Surfaces
Tetmesh Controls in Volumes
Surface Controls: Shape and size of triangles at the boundaries
Volume Controls: Shape and size of tets on the interior
Local Settings: Attribute can be different for each volumes
Global Settings: Attribute is the same for all volumes
Update: View all current settings for selected volumes
Use Default: Change all selected volumes to default settings
Tetmesh Scheme

## Slide 8
Geometry Sizing:
Uses Geometry characteristics to limit size (over-rides entity sizes)
ON by default
Surface Controls
reset
set trimesher geometry sizing off
import acis "crank.sat"
vol 1 scheme tetmesh
vol 1 size auto factor 10
mesh vol 1
delete mesh
set trimesher geometry sizing on
mesh vol 1
Geometry sizing OFF
Geometry sizing ON
Tetmesh Scheme

## Slide 9
Deviation Angle (Geometry Approximation Angle)
Deviation Angle
Deviation Angle
Surface Controls
Tetmesh Scheme

## Slide 10
Deviation Angle (Geometry Approximation Angle)
Surface Controls
Tetmesh Scheme

## Slide 11
Maximum Surface Gradation:
Controls maximum change in triangle sizes from features on the same surface
1.3
1.1
Surface Controls
Tetmesh Scheme

## Slide 12
Maximum Volume Gradation:
Controls maximum change in triangle sizes based in features on other nearby surfaces (proximity)
Surface Controls
Tetmesh Scheme

## Slide 13
Min Tet Layers: Minimum number of tets in narrow regions
Volume Controls
Tetmesh Scheme

## Slide 14
Max Tet Growth Ratio: Tets increase in size from boundaries at this rate
1.0
1.3
Volume Controls
Tetmesh Scheme

## Slide 15
Import model
Import ACIS file driver.sat, cad6.sat OR crank.sat
driver.sat
cad6.sat
1
1
Exercise 9.2 Tetmesh Sizing
Set scheme to tetmesh and mesh with default size
2
crank.sat

## Slide 16
Modify the parameters one at a time and observe the changes to the mesh. (Hit “Use Defaults” button after each mesh)
For example:
Turn off geometry sizing
Min Tet Layers = 2
Deviation angle = 5
Surface Gradation = 1.2
Use the slice tool to see the interior of the mesh
From the command line:
draw tet all
Exercise 9.2 Tetmesh Sizing (continued)
3
4
5

## Slide 17
Curve Biasing
Select Bias and Intervals & Bias
Pick a Curve.
Adjust slide bar to preview biased mesh.
Navigate to Curve Bias Panel
1
2
3
4
Set number of intervals, start vertex, etc..
5
1
2
3
4
5
Propagate Curve Bias
Choose from Bias Scheme on GUI panel
3

## Slide 18
Create the simple model shown using the GUI or command line
Use the procedure shown in the previous slide to generate a biased mesh
Experiment with different options of curve bias
What happens if propagate curve
bias is not applied?
What’s wrong with the interior mesh? (use the slice tool to visualize)
Fix the biasing on the hole surface. (Hint: Webcut with X plane, merge, propagate curve bias)
1
2
Brick x 10 y 10 z 20
Create cylinder height 25 rad 3
Subtract vol 2 from vol 1
3
Exercise 9.3 Curve Biasing
4
webcut volume 1 with plane xplane offset 0