## Slide 1: Geometry for Sweeping
Steven Owen
CUBIT™ 200 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
10
SAND2022-15142 PE

## Slide 2
The Basic CUBIT™ Process
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 3
Source surfaces
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source Surfaces
One or more surfaces
Can be meshed with any Quad Scheme (Pave, Map)
Target Surface
Must be a single surface
Must be unmeshed
Matches topology of source surfaces
Sweep Scheme

## Slide 4
Linking surfaces
Linking surfaces
Linking surfaces
Linking surfaces
Linking Surfaces
Must be “Mappable”
Connect Sources with Target
Sweep Scheme

## Slide 5
Most frequently used meshing scheme
Normally requires geometry to be decomposed to apply sweeping (webcutting)
Sweep Scheme

## Slide 6
Source
Target
Sweep Direction
Multiple
Sources
Target
Multiple
Sources
Multiple
Targets
Sweep Direction
Sweep Direction
One-to-one
Many-to-one
Many-to-many
Sweep Scheme

## Slide 7
What type of sweep scheme is used on each of these meshes?
One-to-one
Many-to-many
One-to-one
Many-to-many
Many-to-one
Many-to-many
Sweep Scheme

## Slide 8
Mesh Power Tools are located on the Entity Tree window under the purple tab.
Meshing Power Tool

## Slide 9
Entities to analyze
Run scheme analysis
Scheme analysis output
Tools for working on model
Meshing Power Tool
Helps identify volumes that are sweepable and those that are not

## Slide 10
Run the mesh scheme analysis on knuckle.sat after cleaning up geometry but before doing any decomposition.
Listed in the power tool window
Displayed Graphically
Results are displayed in two ways
Volume 1 listed under No Scheme Set
Volume 1 is painted Red, indicating no scheme set
Meshing Power Tool Example

## Slide 11
Perform webcuts as needed. After each webcut, run the analysis again to check meshability
Note when a volume moves to the Scheme Set category
Volumes where scheme is set are painted green
Meshing Power Tool Example

## Slide 12
Complete the decomposition
Run imprint and merge
Run the analysis again
Mesh the parts
All volumes should be painted green if schemes successfully set
All volumes should be listed under Scheme Set
Meshing Power Tool Example

## Slide 13: Exercise 10.1 Meshing Power Tool
Import acis “knuckle-defeatured.sat”
Use the meshing power tool to check meshability
Do 3 webcuts, check meshability after each
Imprint and merge
Mesh with hexes using size 1.5
2
1
3
4
5
webcut volume 1 with plane normal to curve 34 close_to vertex 30
webcut volume 2 with plane normal to curve 34 close_to vertex 31
webcut volume 1 3 with plane vertex 25 vertex 28 vertex 20

## Slide 14: Common Techniques for Sweep Decomposition
2. Coring: Core out the center of a cylindrical type object. Use a radial sweep and a top-to-bottom sweep (see exercise 2 from fast-start 10)
3. Multiple sweep directions: Cut to avoid features not in the sweep direction
4. Graded Meshes with pave-sweep: Cut multiple times in direction of grade. Alternate pave-sweep directions
5. Midpoint Subdivision: Cut volumes so the polyhedron scheme can be used
6. Modify surfaces with tweak and composite tools to make volumes sweepable
1. Find One-to-one: Locate the logical one-to-one and many-to-one sweep paths and webcut to isolate (see exercise 1 from fast-start 10)
1.
2.
3.
4.
5.
6.
Sweep Scheme

## Slide 15: Exercise 10.2 Webcut many-to-many sweeps
Mesh the geometry in the file example01.sat with a contiguous all-hex mesh.
Use a mesh size of 0.15
Hints:
Examine sweepability of all volumes. Is there a many-to-many sweep volume?
Don’t forget to imprint and merge
This assembly can be meshed with as little as 1 webcut
CUBIT> webcut volume 5 with sheet extended from surface 70 CUBIT> imprint all CUBIT> merge all CUBIT> volume all size 0.15 CUBIT> volume all scheme auto
webcut volume 5 with sheet extended from surface 70

## Slide 16
Typical one-to-one sweeps
translation
rotation
inside-out
One-to-one sweeping

## Slide 17
Decomposition may require creation of a temporary tool volume to aid in cutting the geometry
A Tool volume is first created and used to webcut the volume
A lofted volume is first created between surface A and B and used as a Tool to cut the volume
A
B
Tool Volume Webcut

## Slide 18: Exercise 10.3 Coring
Mesh the geometry in the file example04.sat with a contiguous all-hex mesh.
Use a mesh size of 0.15
Hints:
Remember to delete the tool volume afterward webcutting
Use a sweep surface webcut to extend the core to the top
Consider a coring approach: Sweep radially around the outside and top to bottom on the interior core.
Split the volumes along a symmetry plane to permit the radial sweep.
Consider creating a tool volume using the loft option for creating volumes to create the core
Remember to imprint and merge!

## Slide 19
source
target
sweep direction
Multiple Sweep Directions

## Slide 20
source
target
sweep direction
One-to-one sweep
“Easy” to mesh
Multiple Sweep Directions

## Slide 21
source
target
sweep direction
What do we do now?
Multiple Sweep Directions

## Slide 22
webcut
sweep direction
Cut around the feature that is stopping us from sweeping
webcut
sweep direction
sweep
direction
In this case we have used the webcut with cylinder tool
Multiple Sweep Directions
sweep direction
sweep direction

## Slide 23: Multiple Sweep Directions
Resulting mesh with 2 sweep directions

## Slide 24: Exercise 10.4 Multiple Sweep Directions
Import the model “blades2.sat”
Generate a mesh with a size of about 2.0
Hint: Use the webcut with cylinder operation to cut out the features that don’t line up with the principal sweep direction

## Slide 25
Fine Mesh
Coarse Mesh
How to generate a graded mesh using sweeping
Sweeping requires a constant number of elements through the entire sweep direction
Sweep Direction
32
32
8
8
But Paving can provide a way to transition the mesh. (However paving is only a 2D procedure)
8
16
Creating a Graded Mesh

## Slide 26
Fine Mesh
Coarse Mesh
How to generate a mesh using sweeping
Webcut the model multiple times along the direction from fine to coarse
32
32
8
8
Creating a Graded Mesh

## Slide 27
Fine Mesh
Coarse Mesh
How to generate a mesh using sweeping
Set up alternating matched intervals on curves
32
32
32
16
16
16
16
8
8
8
Creating a Graded Mesh

## Slide 28
Fine Mesh
Coarse Mesh
How to generate a mesh using sweeping
Alternate pave and sweep directions in each volume
32
32
32
16
16
16
16
8
8
8
Sweep
Sweep
Sweep
Sweep
Pave
Pave
Pave
Pave
Creating a Graded Mesh

## Slide 29: Exercise 10.5 Graded Mesh
Import the model “blades1.sat” and generate a graded mesh. Try grading the mesh from a mesh size of 1.0 to 5.0 as shown here
Size = 1.0
Size = 5.0
Hints:
Use the graded mesh procedure described in the previous slides.
Use the webcut with cylinder operation to cut the geometry.
Try the curve biasing tools to improve the mesh size grading
Try using the “copy mesh” scheme to avoid having to set up the intervals for each paved mesh.
curve 149 size 1
vol 1 size 5
vol 2 size 1
surface 71 scheme pave
Note: When defining bias, use first size and last size. (in command panel first = fine (1.0), last = coarse (5.0))

## Slide 30
Requires 3-valent vertices and convex polyhedron
3D Midpoint subdision
Midpoint Subdivision

## Slide 31
All surfaces must be convex
Midpoint Subdivision

## Slide 32
CUBIT™ will subdivide the geometry into logical mapped regions
Midpoint Subdivision

## Slide 33
A mapped mesh will be applied to each logical region
Midpoint Subdivision

## Slide 34: Exercise 10.6 Midpoint Subdivision
Create a cubit model using the following commands
sphere radius 10
brick x 50
subtract vol 1 from vol 2 keep
delete vol 2
compress all
Mesh the two volumes with a size of 1.0. Make sure the mesh matches between the volumes
Hints: Try cutting the volumes on the 3 coordinate axis. This should result in 16 volumes. You should be able to mesh each of the volumes with scheme Polyhedron. You may want to simplify the model and work on one quadrant, and then use copy/reflect for the other quadrants.

## Slide 35
CUBIT™ includes several tools to modify the surface geometry.
Tools can be used to enforce source-link-target topology for sweeping
Surface Modify Command Panels
Composite
surfaces
Split surfaces
Remove surfaces
Surface Geometry Tools
Surface Context Menu

## Slide 36
Use CUBIT™’s remove surface command to remove and extend the neighboring surfaces
Sweep direction
Remove Surface
Surface Context Menu
(Select a surface – right click)
Remove Surface Command Panel

## Slide 37
Mesh the existing topology gives a poor quality mesh
By splitting the surface and then using virtual geometry will result in a higher quality mesh
Splitting Surfaces

## Slide 38
fillet splits
Sweep direction
Sweep direction
Sweep direction
Watch quality!
Splitting Surfaces

## Slide 39
Use CUBIT™’s split surface command to split fillets down the axis of the fillet
Select surfaces to split
Choose split method (along fillet)
Preview/Apply
Splitting Surfaces

## Slide 40
Virtual Geometry is most often used to cover a set of surfaces which normally prevent the volume from being swept.
This surface is now mappable and can be used as a linking surface.
Note this is a virtual geometry operation
Sweep direction
Surface Context Menu
(Select two or more surfaces – right click)
Composite Surfaces

## Slide 41
Use this button to toggle the dotted line display on virtual composite surfaces
Notice a (v) displayed next to virtual surfaces in the model tree
Use Delete toggle to remove virtual
Composite Surfaces
Surface Context Menu
(Select a composite
surface – right click)
Removing Composites

## Slide 42: Exercise 10.7 Splits and Composites
Mesh the geometry in the file Mbracket.sat with an all-hex mesh. Use a mesh size of about 0.3
Decompostion for sweeping may require multiple sweep directions
At least one of your decomposed volumes should not be sweepable. Try the polyhedron scheme
Hints:
Consider surface modification to improve mesh quality. Try split surface and composite operations
Even though your topology following split/composite is sweepable, CUBIT™ may not recognize it as such. You may need to explicitly set source and target surfaces.