## Slide 1: Sculpt
Steven Owen
CUBIT™ 200 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
15
SAND2022-15142 PE

## Slide 2
Ideal for non-mechanical/
organic shapes
Overlay Grid Method
Uses Cartesian Grid as Base Mesh
Adjusts nodes to geometry
Inserts Layer of Hexes
But can be used for any geometry
Sculpt

## Slide 3
Sculpt is a separate companion application to CUBIT™ .
Can be run from CUBIT™ GUI or in batch from OS command line
Parallel application uses MPI to run on multiple cores/processors
See Cubit 200 for more details/exercises
Does not use Scheme, instead uses Sculpt Parallel command.
Sculpt
3
1
2

## Slide 4
Import the stl file “eros_asteroid.stl” (change the file filter to “stl”)
Preview the overlay grid resolution
Mesh
Use the slice tool to view the interior hexes
2
1
Navigate to sculpt panel
3
4
3
1
5
5
4
3
Sculpt Example

## Slide 5
Overlay Grid Procedure used by Sculpt
Cartesian Grid overlaid on geometry
Nearby nodes projected to boundaries
Mesh pulled away from the boundaries
And Layer of hexes inserted
Smoothing performed to improve element quality
Sculpt Procedure

## Slide 6
CUBIT
sculpt
mpiexec
psculpt
psculpt
psculpt
psculpt
stl
exo
exo
exo
exo
epu
exo
Sculpt Application

## Slide 7
Geometry is first converted to “Volume Fraction” Data before meshing.
Advantages
Geometry Tolerant
No decomposition needed
No imprint/merge needed
Scalable to massive parallel
Disadvantages
No Geometry Associativity
Does not capture corners
“Small” features not resolved
May require large mesh
Sculpt Application
CAD Volume
Volume Fraction Data
Hex Mesh

## Slide 8
Example Sculpt Mesh

## Slide 9
Sculpt Command Panel
sculpt print_help [”<string>”]
Process Control: parallel processors, execution, filenames
Overlay Grid: Cartesian grid description, input mesh
Geometry Definition: Cubit geometry, STL, Diatom, microstructures etc.
Smoothing: Parameters for smoothing
Mesh Parameters: Stair Step, Mesh Void, Hex Dominant
Mesh Improvement: Pillowing, Defeaturing, Capture, Thicken
Adaptivity: Mesh refinement and coarsening criteria
Boundary Conditions: Block and sideset definitions
Mesh Output: Exodus Mesh
Help Options
2
1
3

## Slide 10
Select Blocks or Volumes
Volumes: Each volume treated as a separate mesh. One Block created per volume
Blocks: treat all volumes in block as continuous mesh
Resets values in overlay grid panel back to default. Use this if volumes/blocks change
Base Grid Requires
  Cell Size
  Bounding Box
Select to display preview of bounding box and size
4 ways to define size
Autosize – value 0-10. 0=fine, 10=coarse
Cell size – exact size
Default – use the size defined on the volume. If none then autosize=10
Cartesian Intervals – set the number of intervals in x-y-z directions. Tries to maintain constant aspect ratio
4 ways to define box
Expand Percent: larger than bounding box
Set exact x-y-z bounds
Auto Cartesian – Complete model enclosed in axis-aligned box
Auto Aligned – Sculpt attempts to find a natural orientation of the model with the a fitted box
Note: Fields automatically synchronize to reflect updated user selections
Number of cells in Cartesian Grid
Sculpt Sizing – Cartesian Grid
Resets values in all Sculpt panels

## Slide 11: Example 15.1 Sculpt Cartesian Grid Sizing
Import the ACIS file “crank.sat”
Experiment with different mesh sizes to see its effect. Observe how well it captures the features
.
Use the Auto Align feature. Observe the difference in the resulting mesh
Check the mesh quality
Note the Total Cells estimate. This is total number of cells in the base grid (not mesh size) based on current input. Larger numbers indicate longer meshing times.
Use the Stop button to kill sculpt if meshing time gets too long.
2
1
3
4
quality hex all draw mesh

## Slide 12
Sculpt Input Mesh
In place of a Cartesian grid, Sculpt can also use an arbitrary exodus mesh as the overlay grid
Exodus mesh
(Overlay Grid)
STL geometry
Conformal hex mesh of asteroid embedded in sphere mesh
Sculpt

## Slide 13: Example 15.2 Sculpt Input Mesh
sculpt processors 1 input_mesh "sphere.g" stl_file "eros_asteroid.stl" void 1
2
1
3
4
reset
import stl "eros_asteroid.stl"
sphere rad 30
vol 2 size 0.5
mesh vol 2
block 2 vol 2
export mesh "sphere.g" over
Create an overlay grid mesh from a sphere
Create an overlay grid mesh from a sphere and save the mesh to “sphere.g”
Set the Number of Processors to 1
(Current limitation running from Sculpt)
Set the Overlay grid to “Input Mesh” and select the file“sphere.g”
Set the Geometry type to STL and select the
File “eros_asteroid.g”
Check the Mesh option “mesh void”
Click mesh
5
6
1
sculpt command line
Create an overlay grid mesh from a sphere

## Slide 14
Sculpt Refinement
Sculpt uses an 1:8 refinement procedure.
Specify coarsest size for the overlay grid and number of levels of refinement
Coarse cell size for overlay grid
2 levels of refinement
2 levels of transition
Final smoothed mesh
No refinement
2 Levels
4 Levels
Adapts only where there is curvature in the geometry

## Slide 15: Example 15.3 Sculpt Refinement
Import either “bunny.stl” or “everest.stl”
bunny.stl
everest.stl
Refine by using the default cell size and applying 1 or 2 levels of refinement to capture details of the surfaces
For everest.stl, set the overlay grid
bounding box to exactly match the vertical sides of the model using the “expand percent=0”
For everest.stl also try setting smoothing surface interpolation method to fixed bounding box.
Try meshing with default sizes to begin
Reset the Sculpt panels to Default
2
1
3
4
5
6

## Slide 16
Boundary Conditions
Sculpt can automatically define nodesets, sidesets and blocks on the resulting exodus mesh
Material blocks are most often defined from the input geometry
Cubit Geometry: One block per CUBIT™ Volume
Diatom File: Material identifier in package description
Input Mesh: Can maintain blocks from Exodus input mesh
Microstructures: From volume fraction data
Void space: void_mat option or automatic
Most often defined using one of the gen_sidesets options
fixed: 3 sidesets. Bbox boundary, material free surfaces and material interfaces
variable: Unique surfaces defined bbox boundary, free surfaces and interfaces
geometric_surfaces: From CUBIT™ surface IDs
geometric_sidesets: From CUBIT™ sideset definitions
RVE: for microstructures. At each bbox surface and material interfaces
input_mesh_and_stl: combines sidesets from exodus mesh and diatom file
input_mesh_and_free_surfaces: input_mesh but adds an addition free_surface
rve_variable: Similar to 5, but defines sidesets at unique material interfaces
input_mesh: Builds sidesets from the exodus input_mesh
Blocks
Sidesets
Some options for Nodesets are also offered. Also controlled with gen_sidesets option. See CUBIT™ Sculpt docs
User defines 2 sidesets on the solid model
Sideset 1
(composed of 4 surfaces)
Sideset 2
Sideset 1
Note that sides are only an approximation of the surface. They may not exactly align with bounding curves
Sideset 2
Example:
gen_sidesets = 4

## Slide 17
Sculpt can be run in batch on your local desktop or on an HPC machine
To generate batch input files
1
2
Set your working directory
Click the Sculpt Process Tab
2
3
4
5
Fill in names for files or use default (sculpt_parallel)
3
4
Select Do Not Run Sculpt
Click Preview Input to see the input file contents in the CUBIT™ output window
With the Do Not Run Sculpt option, no mesh will be generated. Instead the batch input files will be written to your working directory
5
Click Mesh button to dump the necessary files to run in batch mode
6
6
Running Sculpt in Batch

## Slide 18
In your working directory you should see the following files
Diatom File: Contains a list of all geometry used as input to Sculpt
Input File: Contains a human readable form of all input parameters to sculpt
Run File: Contains a unix command line script to run sculpt with all parameters
STL File: Triangle-based geometry description. One per volume
Running Sculpt in Batch

## Slide 19
Edit the .i file to view the sculpt input parameters
For a description of parameters, use the –h option on the unix command line
Type:
sculpt
To see a summary of all sculpt options
Type:
sculpt –h <option>
To see help on the any sculpt option
Running Sculpt in Batch

## Slide 20
To run sculpt in batch:
sculpt –i <input file> -j <num_procs>
For example:
sculpt –i asteroid.i -j 4
Observe the mesh summary when the mesh is completed
Number Hexes < 0.0 Scaled Jacobian
Number Hexes < 0.2 Scaled Jacobian
Minimum mesh quality
Running Sculpt in Batch

## Slide 21
Exodus mesh files created (1 per processor)
To combine mesh files:
epu –p <num_procs> <base_file_name>
For example:
epu –p 4 asteroid_mesh
To import mesh into CUBIT™ to view mesh from command line
import mesh "asteroid_mesh.e" no_geom
Running Sculpt in Batch

## Slide 22: Example 15.4 Sculpt Batch
Add a sideset at the boundary of car. Try adding
Build the files needed to run Sculpt from a terminal window for the B3 model using the procedure described. Use the default size. Rename the input file and exodus files to “car”
2
1
3
4
5
6
Import the acis file "B3.sat"
gen_sidesets = fixed
to your input file car.i
Run sculpt from a terminal window with at least 4 processors
Combine the resulting exodus files using epu
Import the resulting mesh into CUBIT™ and check the quality
7
Draw the sideset that was defined in step 3.
draw sideset all
draw sideset all
sculpt –i car.i –j 4
epu –p 4 car
import mesh geom "car.e" no_geom
quality hex all draw mesh

## Slide 23
Microstructures
Material Science applications often use microstructure models defined on a representative volume element (RVE) to simulate the physics of materials. An RVE is normally a cube shaped domain defined as a Cartesian grid, where
each cell of the grid is represented as a material volume fraction. Sculpt can read microstructure information directly and build a geometric model for hex meshing.
Initial voxel representation of polycrystal materials.
Sculpt hex mesh of microstructure
3D polycrystal microstructure
2 phase polymer microstructure
In addition to standard STL and diatoms, several formats for microstructures are supported that contain data on a Cartesian grid. Each cell holds material info for its portion of the grid.
input_micro
input_cart_exo
input_spn
input_stitch
Text format. Once row per cell, One column per material
Exodus File restricted to Hex8 Cartesian grid.
Text file with one integer per cell representing material ID
Sandia supported. SPPARKS and LAMMPS applications
Supported Microstructure Formats

## Slide 24
Microstructures
Spray Foam Material
Elastomeric Syntactic Foam
Crystal Plasticity
Courtesy Judith A. Brown
Courtesy Nathan W. Moore
Courtesy James W. Foulk
Sandia Report: Mesh Generation for Microstructures
https://www.sandia.gov/files/cubit/documents/SculptMicrostructuresSANDReport.pdf
Technical documentation and many examples/use cases

## Slide 25: Example 15.5 Microstructures
Run the input file “sculpt_micro9.i” from a terminal.
1
2
3
sculpt –i sculpt_micro9.i
Import the resulting exodus mesh into cubit as mesh based geometry
import mesh geom “micro_clipped.e.1.0”
delete mesh
vol all size 0.5
vol all scheme tetmesh
mesh vol all
Delete the triangle mesh and generate a tet mesh
Tetmesh
size 2.0
Tetmesh
size 1.0
Tetmesh
size 0.5
Mesh-Based
Geometry